# Implementation Considerations:
- asin, acos functions will return a value on [90,-90] so signs must be considered when using them to find angles whose cos will be needed, i.e.:
  sin(a) =sin(180-a) newline but: newline cos(a) = - cos(180-a)
- fundamental sin equalities :
  sin(a) = sin (180-a) newline sin(90-a) = sin(90+a) newline sin(a) = - sin(-a)

# Tracking Computations

Given inputs:
- AngleR and AngleL, AngleH:
  the angles through which the target appears to the Right and Left Pixies,
- constant B:
  the separation of the 2 pixies
Computation Outputs:
- dx,dy,dz:
  relative offsets of the target with the Observer taken to be the origin. These can be positive or negative
  Y+ is the direction from the observer to the target,
  X+ is the direction from the observer to the right,
  Z+ is the direction from the observer upwards
  Note: the observer drone will be flying in the Y- direction since it will always be ahead of the target.
- B,L,R,d are distances and always positive,
- Pixie offsets are delta and left Pixie is negative offset, right Pixie as positive offset
- al,ar are on ]0,180[
- but a and ap are on ]-90,+90[
- Note that:
  - if the target is perceived to the RIGHT, then dx is NEGATIVE, eg. 0-10 = -10
  - if the target is perceived to the LEFT, then dx >is POSITIVE, eg. 0 - -10 = +10
  - dy is always NEGATIVE, eg. 0 - 10 = -10
  - if the target is perceived ABOVE then, dz is NEGATIVE, eg. 0 - 10= -10
  - if the target is perceived BELOW then, dz is POSITIVE, eg. 0 - -10= +10
## Angles:
al + at + (180 - ar) = 180 newline al + at = ar
at = ar - al
### Sin Law → L and R
{B} over {sin(at)} = {L} over {sin(180-ar)} = {R} over {sin(al)} newline L = {B sin(180-ar)} over {sin( at)} = {B sin(ar)} over {sin( at)} newline R = {B sin(al)} over {sin( at)}

L = {B sin(ar)} over {sin( at)} newline R = {B sin(al)} over {sin( at)}

### Cos Law: → d
d^{2} = L^{2} + ({B}over{2})^{2} - LBcos(al)

d = sqrt{L^{2} + ({B}over{2})^{2} - LBcos(al)}

Projecting on (x,y,z), first we need angle “ap”:

### Sin Law → a
Here we must pay attention since the asin function will always return a value on [-90,90]
{sin(a)} over {R} = {sin(180-ar)}over{d} = {sin(ar)}over{d} newline a = asin({R sin(ar)} over {d}) newline ap = 90 -a

Looking at the sentinel values, we note that:
If:
al < 180 - ar
Then:
we are in looking to the RIGHT case
Else:
we are in the looking to the LEFT (or Center) case.

In the Right case, dx is NEGATIVE!!

if
al < (180 - ar)
then we are in the “RIGHT case”, i.e. dy <0, dx <0
if not:
we are in the “LEFT case” i.e. dy<0, dx>=0

Since we would like to use the same equations for projection, i.e.
dy = d cos (ap) newline dx = d sin(ap)
We need to use the fundamental equalities to adjust ap
if: newline al < 180 - ar newline then: newline ap' = 180 + abs{ap} newline else: newline ap' = 180 - abs{ap} newline dx = d sin(ap') newline dy = d cos(ap')

The height angle “ah” is measured such that:
- ah > 0 when observer is below target, dz > 0
- ah = 0 when observer is at same level as target, dz = 0
- ah < 0 when observer is above target, dz < 0

Then we can find dy and dx and dz:

dx = d sin(ap') newline dy = d cos (ap') newline dz = dy tan(ah)

# Pixie Pixel to Angle Computation

## Pixie Pixel to Angle computations:
The Pixie cameras provide target coordinates in pixels (px,py). It is assumed that the origin of the field of view is lower left.
To compute the Pixie angles in terms of the flown the X-axis and Z-axis, we must do some computation.
Pixie Constants:
- Field of view Angles (fx,fy): values 75° in Pixie X-axis, 47° in Pixie Y-Axis
- Pixel Ranges (rx,ry): values are (640,400)
- Pixie fictive PD: calculated based on the Angles and Pixel ranges.
  PD = {Rg} over {2tan {f}over{2}}
  PD_{x} = {320} over {tan (75/2)} = 417.032119309 newline PD_{y} = {200} over {tan (47/2)} = 459.968509447
Inputs:
- Pixie pixel coordinates of target: (px,py)
- Note: it is assumed that the Pixie measures (0,0) from the lower left corner of its field of view, thus if the target were “dead ahead” the pixie would return (320,200)
- Target dy (Tdy) : distance from Pixie to the target projected onto flown Y-axis
Outputs:
- angle in flown X-axis (a): either 'al' or 'ar' depending on which Pixie
- angle in flown Z-axis (ah)
Computations:
First, let's convert pixel values to a coordinate system based on the origin in the middle of the field of view (320,200), i.e. (RgX/2,RgY/2)
Let's call these coordinates (Npx, Npy):
Npx = x - {RgX} over {2} newline Npy = y - {RgY} over {2}

tan(alpha) = {pix}over{D_pixie} newline if: newline pix >= 0 newline then: newline tan(alpha) >= 0 newline else: newline tan(alpha) < 0

thus:
alpha = arctan({Npx}over{D_px})
and thus we can deduce the required angles from Pixie's ouput!

This maps: Pixie(px,py) → Pixie(a, ah)

a_x = 90 - arctan({Npx}over{D_px}) newline a_h = arctan({Npy}over{D_py})

## Simulation Computations:

In the simulation we know the absolute position of the target and the observer. From that we must compute the data that the Pixies would send to the navigation system.

This means that we must determine the pixel coordinates of the target as seen by each pixie.

The inputs:
Pixie constants:
x-offset: this is the distance in the x-axis that the Pixie is offset from the Observer origin, i.e. B/2 from previous section
Simulation Values:
- Target (x,y,z)
- Observer (x,y,z)
The outputs:
For each Pixie:
Target(px,py): i.e. the pixel values for the coordinates of the target.

From the above computations we can simply factor in the offset of the Pixies, which is in the X-axis and we are golden.

Note that for this computation we take Delta(x,y,z) = Target (x,y,z) - Observer(x,y,z) so as to get the signs to work out right!

dx_p = T_x - (Obs_x + p_{offsetX}) newline dy_p = T_y - Obs_y newline dz_p = T_z - Obs_z

Then noting that we have similar triangles, but still in the Npix frame:
{Npix_x} over {D_px} = {dx}over{dy} newline {Npix_y} over {D_py} = {dz}over{dy}
We have our simulator mapping: T(x,y,z), Obs(x,y,z) → Pixie(px,py) for each Pixie:

px = D_px{dx}over{dy} + {RgX} over {2} newline py = D_py{dz}over{dy} + {RgY} over {2} newline with limit conditions: newline 0<= px <= RgX newline 0 <= py <= RgY newline "in case of non-respect, target is out of view!"
Don't forget to round and cast as integers since pixel values are ints!!!

# Flight controls:

If a2 > 180-a1 then` inc(Vx) newline Elsif a2 < 180-a1 then `dec(Vx) newline Else ` zero(Vx) newline newline If d> D then` inc(Vy) newline Elsif d < D then `dec(Vy) newline Else ` zero(Vy)